## Slide 1: Planning Units
Claire Sherratt

## Slide 2
Thinking about Planning Units
Why is identification of the Planning Unit important?
What to consider when identifying the Planning Unit?
The Enforcement Notice
Grounds of appeal
Appeal Progression – key dates

## Slide 3: The Planning Unit
What is it and why is it important?
Has a material change of use occurred?
As the EPLP states in P55.44:
“The planning unit is a concept which has evolved as a means of determining the most appropriate physical area against which to assess the materiality of change, to ensure consistency in applying the formula of material change of use.”
The general rule has always been that the materiality of change should be assessed in terms of the whole site concerned.

## Slide 4: Identifying the Planning Unit
Physical and Functional separation is key!
In Burdle & Williams v SSE & New Forest DC [1972] 1 WLR 1207, it was held that the planning unit is usually the unit of occupation, unless a smaller area can be identified which, as a matter of fact and degree, is physically separate and distinct, and occupied for different and unrelated purposes; the concept of physical and functional separation is key.
Bridge J suggested three broad categories of distinction:
a) A single planning unit where the unit of occupation has one primary use and any other activities are incidental or ancillary;
b) A single planning unit that is in a mixed use because the land is put to two or more activities and it is not possible to say that one is incidental to another; and
c) The unit of occupation comprises two or more physically separate areas which are occupied for different and unrelated purposes. Each area that has a different primary use ought to be considered as a separate planning unit.
EPL P55.46 states: “Both functional and physical separation are required before a smaller unit can be identified, since without functional separation the ancillary link remains; and without physical separation there is no smaller physical area which can be identified as a separate unit.”

## Slide 5: Identifying the Planning Unit & primary use(s)
Physical and functional links
What is the unit of occupation? The area to be looked at is the whole of that used for a particular purpose, including any part of that area which is put to incidental use.
The area covered by a Planning Permission is not necessarily determinative of the planning unit, although that is likely to be relevant and may be a good starting point.
A use which is authorised by planning permission is capable of being extinguished by the creation of a new planning unit in respect of the land in question
Consider if a smaller area can be identified which, as a matter of fact and degree, is physically separate and distinct, and occupied for different and unrelated purposes?
Subsidiary activities will be incidental uses, which may fluctuate without there necessarily being a MCU of the planning unit.
.

## Slide 6: The Enforcement Notice
The concept of a mixed use is one of two or more primary (or main) uses existing within the same planning unit. One is not incidental to the other.
All of the primary (main) uses that comprise that mixed use of a planning unit should be referred to, not just the one(s) required to cease.
Mixed use
A use which is authorised by planning permission is capable of being extinguished by the creation of a new planning unit in respect of the land in question.
Require the activity complained of to cease along with any works that facilitate that use (caution if a mixed use and some uses remain)
Requirements
Be clear:
Refer to primary (main uses).
The various subsidiary activities will be incidental uses, which may fluctuate without there necessarily being a MCU of the planning unit - be clear if referring to incidental uses..
Alleged breach of planning control
An EN does not have to be directed at the whole unit or indeed to identify it, but it is helpful when it does.
Where the activity complained of only takes place on a small area, the LPA is entitled to anticipate changes to defeat the operation of the notice by enforcing against the planning unit as a whole.
“The Land”
Breach described as the Material Change of Use of the Landl

## Slide 7: Appeal against a Notice directed at a material COU
Ground (b)
Grounds of appeal
The COU is not material. The Inspector would need to consider what the correct planning unit is before determining if there has been a material change of use. A change in the planning unit may be of relevance. Planning permission is capable of being extinguished by the creation of a new planning unit.
Ground (c)
Historic changes in the planning unit and primary uses over relevant period will need to be considered to determine whether it is too late to take enforcement action. Has there been a new chapter in planning history?
Ground (d)
Planning unit relevant to the consideration of the effect of the change in character of activity.
Ground (a)
It is not open to a LPA to divide up a planning unit artificially so as to achieve a more restrictive effect than would result from an EN directed at the unit as a whole.
Ground (f)
That the COU has not occurred.

## Slide 8: Enforcement Appeal progression
Powers now available to the Secretary of State to dismiss an appeal if at any time before or during the determination of an appeal against an EN or LDC it appears to the Secretary of State that the appellant is responsible for undue delay in the progress of the appeal.
Undue delay
Prompt validation of appeal
Inspector appointed at the outset
Case Management Conference held around week 8 of start of appeal
Inquiry event fixed 17-20 weeks from receipt of valid appeal
Enforcement appeal - Inquiries
Focus now on clearing backlogs of WR cases – oldest cases
Increased capacity of Inspectors to accommodate greater number of cases
Normally schedule visits 10-12 weeks ahead at any given time.
Enforcement appeal - Written representations
Prompt validation of appeal
Inspector appointed at outset
Hearing events now fixed 13-16 weeks from receipt of valid appeal
Enforcement appeal - Hearings
Key dates